## Slide 1: Agreement Analysis Tool with R
Amrita Anam
Brandon Gallas
Weijie Chen
Zhiwei Zhang

## Slide 2: Motivation
  Develop a method and a tool
  Calculate and evaluate reader agreement in multi-reader multi-case(MRMC) studies
  Compare pathologists’ performance over different imaging modalities

## Slide 3: Overview
Reader Agreement
Concordance
Intra and Inter Reader
Methodology
Application
Mitotic Count Simulation
Process Overview
Detailed Work Flow
Tool Development
Development Team
Tool Access
Inputs and Outputs
Validation
Example
Results

## Slide 4: Reader Agreement
A measure of agreement
    between 2 readers
    reading a set of cases
    over the same modality

## Slide 5: Reader Agreement – Concordance
Ranking Outcome | Description | Example
Tie in both | scores tied in both conditions | A1 = A2, B1 = B2
Tie in A | scores tied in condition A only | A1 = A2, B1 ≠ B2
Tie in B | scores tied in condition B only | A1 ≠ A2, B1 = B2
Concordance | score for condition A are in the same order as score for condition B | A1 > A2 , B1 > B2
Discordance | scores for condition A are in the opposite order as s for condition B | A1 > A2 , B1 < B2
  Given reading conditions: A and B
  cases: 1 and 2
  scores: A1, A2, B1 and B2

## Slide 6: Reader Agreement: Concordance
  Given
    reading conditions: A and B
    cases: 1 and 2
    scores: A1, A2, B1 and B2
Ranking Outcome | Example
Tie in both | A1 = A2, B1 = B2
Tie in A | A1 = A2, B1 ≠ B2
Tie in B | A1 ≠ A2, B1 = B2
Concordance | A1 > A2 , B1 > B2
Discordance | A1 > A2 , B1 < B2

## Slide 7: Reader Agreement
Intra Reader Agreement
Intra Modality Agreement
Inter Modality Agreement
Inter Reader Agreement
Intra Modality Agreement
Inter Modality Agreement
Needs Replication

## Slide 8: Reader Agreement
Notes:
  Averaging in different areas
  MRMC analysis: account for variability from readers and cases
Intra Reader Agreement
Inter Reader Agreement

## Slide 9: Application: HER-2 Study
Marios’ study to analyze the impact of CAD on HER-2 evaluation [1][2]
Readers | 14 (7 pathologists, 7 novices)
Cases | Study 1 – 241 in both modalities (no replication) Study 2 – 47 in both modalities (with replication)
Modalities | Unaided, Aided with CAD
Study Design | Fully Crossed (Every reader reads every case in both modalities)
[1] Gavrielides, Marios A., et al. "Observer performance in the use of digital and optical microscopy for the interpretation of tissue-based biomarkers."Analytical Cellular Pathology 2014 (2014).
[2]Lenz, Petra, and Stephen M. Hewitt. "Observer variability in the interpretation of HER2/neu immunohistochemical expression with unaided and computer-aided digital microscopy." Archives of pathology & laboratory medicine 135.2 (2011): 233.

## Slide 10: HER-2 Study: Reader Agreement
Inter Reader Readers = 14 Cases = 241 |  | Kendall [1] | Concordance
Unaided | Agreement | 0.62 | 0.78
 | Confidence Interval | 0.56 – 0.67 | 0.76 – 0.81
Aided | Agreement | 0.76 | 0.85
 | Confidence Interval | 0.71 – 0.81 | 0.82 – 0.88
Difference | Agreement | 0.14 | 0.069
 | Confidence Interval | 0.10 – 0.19 | 0.052 - 0.087
Inter Reader Readers = 14 Cases = 241 |  |  | Concordance
Unaided | Agreement | 0.62 | 0.78
 | Confidence Interval | 0.56 – 0.67 | 0.76 – 0.81
Aided | Agreement | 0.76 | 0.85
 | Confidence Interval | 0.71 – 0.81 | 0.82 – 0.88
Difference | Agreement | 0.14 | 0.069
 | Confidence Interval | 0.10 – 0.19 | 0.052 - 0.087
[1]Lenz, Petra, and Stephen M. Hewitt. "Observer variability in the interpretation of HER2/neu immunohistochemical expression with unaided and computer-aided digital microscopy." Archives of pathology & laboratory medicine 135.2 (2011): 233.

## Slide 11: Method Development
U-statistics are used to estimate agreement and its variance
Simulation is used to validate variance estimates
    Explore different experiment sizes
    Explore different simulation configurations
    Explore different relative weights of noises
Methods treat fully-crossed data and split-plot studies

## Slide 12: Mitotic Count Simulation
Set input parameters (size and model)
Simulate survival time and censoring time
Determine Mean Mitotic Count
Simulate Random Effects: Readers, Cases, Locations (Replicates)
Calculate Agreement Measure and Estimate the variance
Repeat process for all MC trials

## Slide 13: Mitotic Count Simulation: Work Flow

## Slide 14: Tool Development: GitHub
Development Team
  Mitotic Count Simulation – Amrita
  Intra Reader Agreement – Weijie
  Inter Reader Agreement – Brandon
  Reader Truth Agreement – Zhiwei
  Validation and Integration – Amrita

## Slide 15: Tool Development
Software Specification
Language : R (can be installed from https://cran.r-project.org/)
Supported OS : windows/mac/linux
Access : GitHub
Application : https://github.com/DIDSR/mitoticCountSimulation/releases
Source Code : https://github.com/DIDSR/mitoticCountSimulation/tree/master
Software Manual: http://didsr.github.io/mitoticCountSimulation/

## Slide 16: Tool Development: Simulation and Agreement
Controls:
  Study Design
      Fully Crossed
      Split Plot
  Replication
  Study Size
  Simulation Configuration
Fully Crossed
Split Plot
No Replication
Replication

## Slide 17: Tool Development: Mitotic Count Simulation
Input
  Accept input from a file
  Contains 16 parameters
  Description is given in the sample input file

## Slide 18: Tool Development - Input Components
Output Flags (0/1)
mod0var, modAvar, modBvar = Effects with and without modality
reader-unit/location (within a case) effect
reader-case effect
unit/location (within a case) effect
case effect
mrmcout = save simulation outputs
plotout = save Survival time Vs. Mitotic Counts for one MC trial
meancounts = fixed effect for each modality
Random Effects
Fixed Effects
agreementout = save agreement measures
reader effect
Random Number Generator
Study Size and Design for Simulation
Means for Truth Simulation
seed = integer to initiate RNG
Nr = Number of readers
Nc = Number of cases
Nu = Number of units/locations
Nm = Number of modalities (tests)
Ng = Number of groups for Split plot
meansurvtime = mean survival time
Nmc = Number of Monte Carlo Simulations to be generated
meancentime = mean censoring time

## Slide 19: Tool Development - Output
MRMC Output
plotout
Count VS. Survival Time
agreementout
Agreement Measures
mrmcout

## Slide 20: Example Study: Simulation Inputs
seed = 10
Nmc = 10000
Nr = 12
Nc = 120
Nu = 2
Nm = 2
Ng = 3
meansurvtime = 1000
meancentime = 500
meancount = 5, 6
mod0var = 0.1, 0.1, 0.1, 0.1, 0.1
modAvar = 0.1, 0.1, 0.1, 0.1, 0.1
modBvar = 0.1, 0.1, 0.1, 0.1, 0.1

## Slide 21: First Validation Experiment
Fully Crossed
Split Plot
Readers = 12
Cases = 120
Readers = 4
Cases = 40
Groups = 3

## Slide 22: Intra-Reader Agreement - Fully Crossed
Readers = 12 Cases = 120 MC Trials = 10,000 |  | Intra Modality | Inter Modality
Concordance | Mean | 0.9230058 | 0.807092
 | Variance | 0.0000459 | 0.0000454
Variance Estimates | Mean | 0.0000457 | 0.0000458
 | Variance | 2.069e-10 | 2.037e-10

## Slide 23: Inter-Reader Agreement - Fully Crossed
Readers = 12 Cases = 120 MC Trials = 10,000 |  | Intra Modality | Inter Modality
Concordance | Mean | 0.9055458 | 0.9054926
 | Variance | 0.0000620 | 0.0000614
Variance Estimates | Mean | 0.0000617 | 0.0000617
 | Variance | 3.676e-10 | 3.658e-10

## Slide 24: Intra-Reader Agreement - Split Plot
Readers = 12 Cases = 120 MC Trials = 10,000 |  | Intra Modality | Inter Modality
Concordance | Mean | 0.817427 | 0.824167
 | Variance | 0.000188 | 0.000166
Variance Estimates | Mean | 0.000185 | 0.000164
 | Variance | 6.74E-09 | 5.25E-09

## Slide 25: Inter-Reader Agreement - Split Plot
Readers = 12 Cases = 120 MC Trials = 10,000 |  | Intra Modality | Inter Modality
Concordance | Mean | 0.815621 | 0.807092
 | Variance | 0.000204 | 0.000175
Variance Estimates | Mean | 0.000199 | 0.000172
 | Variance | 3.27E-08 | 2.38E-08

## Slide 26: Status and Future Work
Release R Package
    Simulation
    Agreement
    Plots
NIH Study
Censored data impacts reader vs. truth agreement
Distribute the work at SPIE and Publish!

## Slide 27: Acknowledgements
Brandon Gallas
Qi Gong
To-Oanh
Weijie Cheng
Zhiwei Zhang
Kyle J. Myers
Aldo Badano
Nicholas Petrick
Marios Gavrielides

## Slide 28: Thank You